## Slide 1: Chapter 4: Network layer

## Slide 2: Chapter 4: network layer
chapter goals:
understand principles behind network layer services:
  network layer service models
  forwarding versus routing
  how a router works
  routing (path selection)
  broadcast, multicast
instantiation, implementation in the Internet

## Slide 3
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 4: Network layer
transport segment from sending to receiving host
on sending side encapsulates segments into datagrams
on receiving side, delivers segments to transport layer
network layer protocols in every host, router
router examines header fields in all IP datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 5: Two key network-layer functions
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to dest.
  routing algorithms
analogy:
routing: process of planning trip from source to dest
forwarding: process of getting through single interchange

## Slide 6
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
Interplay between routing and forwarding
routing algorithm determines
end-end-path through network
forwarding table determines
local forwarding at this router

## Slide 7: Connection setup
3rd important function in some network architectures:
  ATM, frame relay, X.25
before datagrams flow, two end hosts and intervening routers establish virtual connection
  routers get involved
network vs transport layer connection service:
  network: between two hosts (may also involve intervening routers in case of VCs)
  transport: between two processes

## Slide 8: Network service model
Q: What service model for “channel” transporting datagrams from sender to receiver?
example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing

## Slide 9: Network layer service models:
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?

## Slide 10
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 11: Connection, connection-less service
datagram network provides network-layer connectionless service
virtual-circuit network provides network-layer connection service
analogous to TCP/UDP connecton-oriented / connectionless transport-layer services, but:
  service: host-to-host
  no choice: network provides one or the other
  implementation: in network core

## Slide 12: Virtual circuits
call setup, teardown for each call before data can flow
each packet carries VC identifier (not destination host address)
every router on source-dest path maintains “state” for each passing connection
link, router resources (bandwidth, buffers) may be allocated to VC (dedicated resources = predictable service)
“source-to-dest path behaves much like telephone circuit”
  performance-wise
  network actions along source-to-dest path

## Slide 13: VC implementation
a VC consists of:
  path from source to destination
  VC numbers, one number for each link along path
  entries in forwarding tables in routers along path
packet belonging to VC carries VC number (rather than dest address)
VC number can be changed on each link.
  new VC number comes from forwarding table

## Slide 14: VC forwarding table
12
22
32
1
2
3
VC number
interface
number
Incoming interface Incoming VC # Outgoing interface Outgoing VC #
1 12 3 22
2 63 1 18
3 7 2 17
1 97 3 87
… … … …
forwarding table in
northwest router:
VC routers maintain connection state information!

## Slide 15: Virtual circuits: signaling protocols
application
transport
network
data link
physical
used to setup, maintain teardown VC
used in ATM, frame-relay, X.25
not used in today’s Internet
1. initiate call
2. incoming call
3. accept call
4. call connected
5. data flow begins
6. receive data
application
transport
network
data link
physical

## Slide 16: Datagram networks
no call setup at network layer
routers: no state about end-to-end connections
  no network-level concept of “connection”
packets forwarded using destination host address
1. send datagrams
application
transport
network
data link
physical
application
transport
network
data link
physical
2. receive datagrams

## Slide 17: Datagram forwarding table
1
2
3
IP destination address in
arriving packet’s header
routing algorithm
local forwarding table
dest address
output link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
4 billion IP addresses, so rather than list individual destination address
list range of addresses
(aggregate table entries)

## Slide 18: Datagram forwarding table
Destination Address Range
11001000 00010111 00010000 00000000
through
11001000 00010111 00010111 11111111
11001000 00010111 00011000 00000000
through
11001000 00010111 00011000 11111111
11001000 00010111 00011001 00000000
through
11001000 00010111 00011111 11111111
otherwise
Link Interface
0
1
2
3
Q: but what happens if ranges don’t divide up so nicely?

## Slide 19: Longest prefix matching
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface?
which interface?
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix matching
Link interface
0
1
2
3

## Slide 20: Datagram or VC network: why?
Internet (datagram)
data exchange among computers
  “elastic” service, no strict timing req.
many link types
  different characteristics
  uniform service difficult
“smart” end systems (computers)
  can adapt, perform control, error recovery
  simple inside network, complexity at “edge”
ATM (VC)
evolved from telephony
human conversation:
  strict timing, reliability requirements
  need for guaranteed service
“dumb” end systems
  telephones
  complexity inside network

## Slide 21
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 22: Interplay between routing, forwarding
1
2
3
IP destination address in
arriving packet’s header
routing algorithm
local forwarding table
dest address
output link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
routing algorithm determines
end-end-path through network
forwarding table determines
local forwarding at this router

## Slide 23: Graph abstraction
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
aside: graph abstraction is useful in other network contexts, e.g.,
P2P, where N is set of peers and E is set of TCP connections

## Slide 24: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or inversely related to
congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least cost path

## Slide 25: Routing algorithm classification
Q: global or decentralized information?
global:
all routers have complete topology, link cost info
“link state” algorithms
decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms
Q: static or dynamic?
static:
routes change slowly over time
dynamic:
routes change more quickly
  periodic update
  in response to link cost changes

## Slide 26
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 27: A Link-State Routing Algorithm
Dijkstra’s algorithm
net topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (‘source”) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k dest.’s
notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current value of cost of path from source to dest. v
p(v): predecessor node along path from source to v
N': set of nodes whose least cost path definitively known

## Slide 28: Dijsktra’s Algorithm
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'

## Slide 29
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Dijkstra’s algorithm: example
Step
N'
D(v)
p(v)
0
1
2
3
4
5
D(w)
p(w)
D(x)
p(x)
D(y)
p(y)
D(z)
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
notes:
construct shortest path tree by tracing predecessor nodes
ties can exist (can be broken arbitrarily)
uwxvyz

## Slide 30: Dijkstra’s algorithm: another example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 31: Dijkstra’s algorithm: example (2)
u
y
x
w
v
z
resulting shortest-path tree from u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
link
resulting forwarding table in u:

## Slide 32: Dijkstra’s algorithm, discussion
algorithm complexity: n nodes
each iteration: need to check all nodes, w, not in N
n(n+1)/2 comparisons: O(n2)
more efficient implementations possible: O(nlogn)
oscillations possible:
e.g., support link cost equals amount of carried traffic:
A
D
C
B
1
1+e
e
0
e
1
1
0
0
initially
A
D
C
B
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
A
D
C
B
given these costs,
find new routing….
resulting in new costs
0
2+e
1+e
1
0
0
A
D
C
B
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1

## Slide 33
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 34: Distance vector algorithm
Bellman-Ford equation (dynamic programming)
let
dx(y) := least-cost path from x to y
then
dx(y) = min {c(x,v) + dv(y) }
v
cost to neighbor v
min taken over all neighbors v of x
cost from neighbor v to destination y

## Slide 35: Bellman-Ford example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
dv(Z) least cost path through the neighbor v to z
Add this along with the costs from u to v ie c(u,v)=2,c(u,x)=1 and c(u,w)=5 this all values are subtituted in
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
node achieving minimum is next
hop in shortest path, used in forwarding table
B-F equation says:

## Slide 36: Distance vector algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
With DV algm each node x maintains the following routing infrm.
  For each neighbor V the cost c(x,v)from x to directly attached neighbor v
  Node x’s distance vector ie Dx = [Dx(y): y є N
  containing x’s estimate of its cost to all destn Y in N
  maintains its neighbors’ distance vectors. For each neighbor v, x maintains Dv = [Dv(y): y є N ]

## Slide 37: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
V =one of the neighboring node.
Dv(y)=least cost distance from V to Y ie
If v=y Dx(y) ← minv{c(x,v) + Dv(y)}

## Slide 38
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from

## Slide 39
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from

## Slide 40: Distance vector algorithm
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
each node:

## Slide 41
Distance vector algorithm
At each node X:
1 Initialization:
2 For all destination y in N:
3 Dx(y)=c(x,y)/* if y is not a neighbor then c(x,y)= ∞ */
4 For each neighbor W
5 Dw(y)=? For all destinations y in N
6 For each neighbor W
7 send distance vector Dx = [Dx(y): y in N] to W]
8
9 Loop
Wait (until I see a link cost change to some neighbor w or
Until I receive a distance vector from some neighbor w)
12
13 For each y in N:
14 Dx(y) ← minv{c(x,v) + Dv(y)}
15 If Dx(y) changed for any destination y
16 Send distance vector Dx = [Dx(y): y in N] to all neighbors
17 forever.

## Slide 42: Distance vector: link cost changes
link cost changes:
node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbors
“good
news
travels
fast”
x
z
1
4
50
y
1
t0 : y detects link-cost change, updates its DV, informs its neighbors.
t1 : z receives update from y, updates its table, computes new least cost to x , sends its neighbors its DV.
t2 : y receives z’s update, updates its distance table. y’s least costs do not change, so y does not send a message to z.

## Slide 43: Distance vector: link cost changes
link cost changes:
node detects local link cost change
bad news travels slow - “count to infinity” problem!
44 iterations before algorithm stabilizes: see text
x
z
1
4
50
y
60
poisoned reverse:
If Z routes through Y to get to X :
  Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
will this completely solve count to infinity problem?

## Slide 44: Comparison of LS and DV algorithms
message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
  convergence time varies
speed of convergence
LS: O(n2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network

## Slide 45
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 46: Hierarchical routing
scale: with 600 million destinations:
can’t store all dest’s in routing tables!
routing information exchange using LS and DV algorithm will increase the complexity of ropute computation when internet consists of hundreds of millions of hosts.
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network

## Slide 47: Hierarchical routing
aggregate routers into regions, “autonomous systems” (AS)
routers in same AS run same routing protocol
  “intra-AS” routing protocol
  routers in different AS can run different intra-AS routing protocol
gateway router:
at “edge” of its own AS
has link to router in another AS

## Slide 48: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
forwarding table configured by both intra- and inter-AS routing algorithm
  intra-AS sets entries for internal dests
  inter-AS & intra-AS sets entries for external dests

## Slide 49: Inter-AS tasks
suppose router in AS1 receives datagram destined outside of AS1:
  router should forward packet to gateway router, but which one?
AS1 must:
learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
job of inter-AS routing!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks

## Slide 50: Example: setting forwarding table in router 1d
suppose AS1 learns (via inter-AS protocol) that subnet x reachable via AS3 (gateway 1c), but not via AS2
  inter-AS protocol propagates reachability info to all internal routers
router 1d determines from intra-AS routing info that its interface I is on the least cost path to 1c
  installs forwarding table entry (x,I)
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
x
…

## Slide 51: Example: choosing among multiple ASes
now suppose AS1 learns from inter-AS protocol that subnet x is reachable from AS3 and from AS2.
to configure forwarding table, router 1d must determine which gateway it should forward packets towards for dest x
  this is also job of inter-AS routing protocol!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
x
……
…
?

## Slide 52: Example: choosing among multiple ASes
learn from inter-AS
protocol that subnet
x is reachable via
multiple gateways
use routing info
from intra-AS
protocol to determine
costs of least-cost
paths to each
of the gateways
hot potato routing:
choose the gateway
that has the
smallest least cost
determine from
forwarding table the
interface I that leads
to least-cost gateway.
Enter (x,I) in
forwarding table
now suppose AS1 learns from inter-AS protocol that subnet x is reachable from AS3 and from AS2.
to configure forwarding table, router 1d must determine towards which gateway it should forward packets for dest x
  this is also job of inter-AS routing protocol!
hot potato routing: send packet towards closest of two routers.

## Slide 53
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 54: Intra-AS Routing
also known as interior gateway protocols (IGP)
most common intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary)

## Slide 55: RIP ( Routing Information Protocol)
included in BSD-UNIX distribution in 1982
distance vector algorithm
  distance metric: # hops (max = 15 hops), each link has cost 1
  DVs exchanged with neighbors every 30 sec in response message (aka advertisement)
  each advertisement: list of up to 25 destination subnets (in IP addressing sense)
D
C
B
A
u
v
w
x
y
z
subnet hops
u 1
v 2
w 2
x 3
y 3
z 2
from router A to destination subnets:

## Slide 56: RIP: example
destination subnet next router # hops to dest
w A 2
y B 2
z B 7
x -- 1
…. …. ....
routing table in router D
w
x
y
z
A
C
D
B

## Slide 57: RIP: example
w
x
y
z
A
C
D
B
destination subnet next router # hops to dest
w A 2
y B 2
z B 7
x -- 1
…. …. ....
routing table in router D
A
5
dest next hops
w - 1
x - 1
z C 4
…. … ...
A-to-D advertisement

## Slide 58: RIP: link failure, recovery
if no advertisement heard after 180 sec --> neighbor/link declared dead
  routes via neighbor invalidated
  new advertisements sent to neighbors
  neighbors in turn send out new advertisements (if tables changed)
  link failure info quickly (?) propagates to entire net
  poison reverse used to prevent ping-pong loops (infinite distance = 16 hops)

## Slide 59: RIP table processing
RIP routing tables managed by application-level process called route-d (daemon)
advertisements sent in UDP packets, periodically repeated
physical
link
network forwarding
(IP) table
transport
(UDP)
routed
physical
link
network
(IP)
transprt
(UDP)
routed
forwarding
table

## Slide 60: OSPF (Open Shortest Path First)
“open”: publicly available
uses link state algorithm
  LS packet dissemination
  topology map at each node
  route computation using Dijkstra’s algorithm
OSPF advertisement carries one entry per neighbor
advertisements flooded to entire AS
  carried in OSPF messages directly over IP (rather than TCP or UDP
IS-IS routing protocol: nearly identical to OSPF

## Slide 61: OSPF “advanced” features (not in RIP)
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
for each link, multiple cost metrics for different TOS (e.g., satellite link cost set “low” for best effort ToS; high for real time ToS)
integrated uni- and multicast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
hierarchical OSPF in large domains.

## Slide 62: Hierarchical OSPF
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers

## Slide 63: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS’s.

## Slide 64: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASs.
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy.
allows subnet to advertise its existence to rest of Internet: “I am here”

## Slide 65: BGP basics
when AS3 advertises a prefix to AS1:
  AS3 promises it will forward datagrams towards that prefix
  AS3 can aggregate prefixes in its advertisement
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
BGP session: two BGP routers (“peers”) exchange BGP messages:
  advertising paths to different destination network prefixes (“path vector” protocol)
  exchanged over semi-permanent TCP connections
BGP
message

## Slide 66: BGP basics: distributing path information
AS3
AS2
3b
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
using eBGP session between 3a and 1c, AS3 sends prefix reachability info to AS1.
  1c can then use iBGP do distribute new prefix info to all routers in AS1
  1b can then re-advertise new reachability info to AS2 over 1b-to-2a eBGP session
when router learns of new prefix, it creates entry for prefix in its forwarding table.
eBGP session
iBGP session

## Slide 67: Path attributes and BGP routes
advertised prefix includes BGP attributes
  prefix + attributes = “route”
two important attributes:
  AS-PATH: contains ASs through which prefix advertisement has passed: e.g., AS 67, AS 17
  NEXT-HOP: indicates specific internal-AS router to next-hop AS. (may be multiple links from current AS to next-hop-AS)
gateway router receiving route advertisement uses import policy to accept/decline
  e.g., never route through AS x
  policy-based routing

## Slide 68: BGP route selection
router may learn about more than 1 route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 69: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to peer and authenticates sender
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 70: BGP routing policy
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two networks
  X does not want to route from B via X to C
  .. so X will not advertise to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 71: BGP routing policy (2)
A advertises path AW to B
B advertises path BAW to X
Should B advertise path BAW to C?
  No way! B gets no “revenue” for routing CBAW since neither W nor C are B’s customers
  B wants to force C to route to w via A
  B wants to route only to/from its customers!
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 72: Why different Intra-, Inter-AS routing ?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its net.
intra-AS: single admin, so no policy decisions needed
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy may dominate over performance

## Slide 73
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 74: 14.1 Introduction: Unicasting
Figure 14-1
In unicast routing, the router forwards
the received packet through
only one of its interfaces.

## Slide 75: Broadcast routing
R1
R2
R3
R4
source duplication
R1
R2
R3
R4
in-network
duplication
duplicate
creation/transmission
duplicate
duplicate
deliver packets from source to all other nodes
source duplication is inefficient:
source duplication: how does source determine recipient addresses?

## Slide 76: In-network duplication
flooding: when node receives broadcast packet, sends copy to all neighbors
  problems: cycles & broadcast storm
controlled flooding: node only broadcasts pkt if it hasn’t broadcast same packet before
  node keeps track of packet ids already broadacsted
  or reverse path forwarding (RPF): only forward packet if it arrived on shortest path between node and source
spanning tree:
  no redundant packets received by any node

## Slide 77: Spanning tree
A
B
G
D
E
c
F
A
B
G
D
E
c
F
(a) broadcast initiated at A
(b) broadcast initiated at D
first construct a spanning tree
nodes then forward/make copies only along spanning tree

## Slide 78: Spanning tree: creation
A
B
G
D
E
c
F
1
2
3
4
5
stepwise construction of spanning tree (center: E)
A
B
G
D
E
c
F
(b) constructed spanning tree
center node
each node sends unicast join message to center node
  message forwarded until it arrives at a node already belonging to spanning tree

## Slide 79
Figure 14-2
Multicasting
In multicast routing, the router may forward the received packet through several of its interfaces.

## Slide 80: Multicast routing: problem statement
goal: find a tree (or trees) connecting routers having local mcast group members
tree: not all paths between routers used
shared-tree: same tree used by all group members
shared tree
source-based trees
group
member
not group
member
router
with a
group
member
router
without
group
member
legend
source-based: different tree from each sender to rcvrs
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-9

## Slide 81: Approaches for building mcast trees
approaches:
source-based tree: one tree per source
  shortest path trees
  reverse path forwarding
group-shared tree: group uses one tree
  minimal spanning (Steiner)
  center-based trees
…we first look at basic approaches, then specific protocols adopting these approaches
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-11

## Slide 82: Shortest path tree
mcast forwarding tree: tree of shortest path routes from source to all receivers
  Dijkstra’s algorithm
i
router with attached
group member
router with no attached
group member
link used for forwarding,
i indicates order link
added by algorithm
LEGEND
R1
R2
R3
R4
R5
R6
R7
2
1
6
3
4
5
s: source
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-12

## Slide 83
Figure 14-5
Reverse Path Forwarding
In reverse path forwarding (RPF), the router forwards only the packets that have traveled the shortest path from the source to the router; all other copies are discarded. No Loops

## Slide 84: IGMP
In multicast routing, Packets from remote sources will only be forwarded by IP routers onto a local network only if they know there is at least one recipient for that group on that network.
Internet Group Management Protocol (IGMP)
  Used by end hosts to signal that they want to join a specific multicast group.
  Used by routers to discover what groups have interested member hosts on each network to which they are attached.
  Implemented directly over IP.

## Slide 85: Reverse path forwarding: example
result is a source-specific reverse SPT
  may be a bad choice with asymmetric links
router with attached
group member
router with no attached
group member
datagram will be forwarded
LEGEND
R1
R2
R3
R4
R5
R6
R7
s: source
datagram will not be
forwarded
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-14

## Slide 86: Reverse path forwarding: pruning
forwarding tree contains subtrees with no mcast group members
  no need to forward datagrams down subtree
  “prune” msgs sent upstream by router with no downstream group members
router with attached
group member
router with no attached
group member
prune message
LEGEND
links with multicast
forwarding
P
R1
R2
R3
R4
R5
R6
R7
s: source
P
P
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-15

## Slide 87: Center-based trees
single delivery tree shared by all
one router identified as “center” of tree
to join:
  edge router sends unicast join-msg addressed to center router
  join-msg “processed” by intermediate routers and forwarded towards center
  join-msg either hits existing tree branch for this center, or arrives at center
  path taken by join-msg becomes new branch of tree for this router
Notes: Notes:
1. It’s always nice to see a PhD dissertation with impact. The earliest discussion of center-based trees for multicast appears to be D. Wall, “Mechanisms for Broadcast and Selective Broadcast,” PhD dissertation, Stanford U., June 1980.
3.3 Network Layer: Multicast Routing Algorithms 3-17

## Slide 88
In CBT, the source sends the multicast packet (encapsulated in a unicast packet) to the core router. The core router decapsulates the packet and forwards it to all interested hosts.

## Slide 89: Center-based trees: example
suppose R6 chosen as center:
router with attached
group member
router with no attached
group member
path order in which join messages generated
LEGEND
2
1
3
1
R1
R2
R3
R4
R5
R6
R7
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-18

## Slide 90: Internet Multicasting Routing: DVMRP
DVMRP: distance vector multicast routing protocol, RFC1075
flood and prune: reverse path forwarding, source-based tree
  RPF tree based on DVMRP’s own routing tables constructed by communicating DVMRP routers
  no assumptions about underlying unicast
  initial datagram to mcast group flooded everywhere via RPF
  routers not wanting group: send upstream prune msgs
Notes: Notes:
D. Waitzman, S. Deering, C. Partridge, “Distance Vector Multicast Routing Protocol,” RFC 1075, Nov. 1988. The version of DVMRP in use today is considerably enhanced over the RFC1075 spec.
A more up-to-date “work-in-progress” defines a version 3 of DVMRP: T. Pusateri, “Distance Vector Multicast Routing Protocol,” work-in-progress, draft-ietf-idmr-v3-05.ps
3.4 Network Layer: Internet Multicast Routing Algorithms 3-20

## Slide 91: DVMRP: continued…
soft state: DVMRP router periodically (1 min.) “forgets” branches are pruned:
  mcast data again flows down unpruned branch
  downstream router: reprune or else continue to receive data
routers can quickly regraft to tree
  following IGMP join at leaf
odds and ends
  commonly implemented in commercial router
Notes: Notes:
1. See www.mbone.com/mbone/routers.html for a (slightly outdatet) list of multicast capable routers (supporting DVMPR as well as other protocols) from various vendors.
2. ftp://parcftp.xerox.com/pub/net-research/ipmulti for circa 1996 public copy “mrouted” v3.8 of DVMRP routing software for various workstation routing platforms.
3.4 Network Layer: Internet Multicast Routing Algorithms 3-21

## Slide 92: PIM: Protocol Independent Multicast
not dependent on any specific underlying unicast routing algorithm (works with all)
two different multicast distribution scenarios :
dense:
group members densely packed, in “close” proximity.
bandwidth more plentiful
sparse:
# networks with group members small wrt # interconnected networks
group members “widely dispersed”
bandwidth not plentiful
Notes: Notes:
a very readable discussion of the PIM architecture is S. Deering, D. Estrin, D. Faranacci, V. Jacobson, C. Liu, L. Wei, “The PIM Architecture for Wide Area Multicasting,” IEEE/ACM Transactions on Networking, Vol. 4, No. 2, April 1996.
D. Estrin et al, PIM-SM: Protocol Specification, RFC 2117, June 1997
S. Deering et al, PIM Version 2, Dense Mode Specification, work in progress, draft-ietf-idmr-pim-dm-05.txt
PIM is implemented in Cisco routers and has been deployed in UUnet as part of their streaming multimedia delivery effort. See S. LaPolla, “IP Multicast makes headway among ISPs,” PC Week On-Line, http://www.zdnet.com/pcweek/news/1006/06isp.html
3.4 Network Layer: Internet Multicast Routing Algorithms 3-25

## Slide 93: Protocol Independent Multicast
Protocol Independent Multicast (PIM) is the name given to two independent multicast routing protocols:
  Protocol Independent Multicast, Dense Mode (PIM-DM), and
  Protocol Independent Multicast, Sparse Mode (PIM-SM).
Dense mode (PIM-DM):
  Uses source-based trees.
  PIM-DM uses RPF and pruning/grafting strategies to handle multicasting.
  It is independent from the underlying unicast protocol.
  Used in a dense multicast environment, such as a LAN environment.
Sparse mode (PIM-SM):
  Uses shared trees.
  PIM-SM is used in a sparse multicast environment such as a WAN.
  PIM-SM is similar to CBT but uses a simpler procedure.

## Slide 94: PIM- dense mode
flood-and-prune RPF: similar to DVMRP but…
underlying unicast protocol provides RPF info for incoming datagram
less complicated (less efficient) downstream flood than DVMRP reduces reliance on underlying routing algorithm
has protocol mechanism for router to detect it is a leaf-node router
Notes: Notes:
3.4 Network Layer: Internet Multicast Routing Algorithms 3-27

## Slide 95: PIM - sparse mode
center-based approach
router sends join msg to rendezvous point (RP)
  intermediate routers update state and forward join
after joining via RP, router can switch to source-specific tree
  increased performance: less concentration, shorter paths
all data multicast
from rendezvous
point
rendezvous
point
join
join
join
R1
R2
R3
R4
R5
R6
R7
Notes: Notes:
3.4 Network Layer: Internet Multicast Routing Algorithms 3-28

## Slide 96: PIM - sparse mode
sender(s):
unicast data to RP, which distributes down RP-rooted tree
RP can extend mcast tree upstream to source
RP can send stop msg if no attached receivers
  “no one is listening!”
all data multicast
from rendezvous
point
rendezvous
point
join
join
join
R1
R2
R3
R4
R5
R6
R7
Notes: Notes:
3.4 Network Layer: Internet Multicast Routing Algorithms 3-29

## Slide 97
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format, IPv4 addressing, ICMP, IPv6
4.5 routing algorithms
  link state, distance vector, hierarchical routing
4.6 routing in the Internet
  RIP, OSPF, BGP
4.7 broadcast and multicast routing
Chapter 4: done!
understand principles behind network layer services:
  network layer service models, forwarding versus routing how a router works, routing (path selection), broadcast, multicast
instantiation, implementation in the Internet